La BlueFrog-V2

Low-level API Contents
Release 0.a

Note : the .h files that expose the functions, types and macros defined below are located under …/libraries/BlueFrogV2-Lib/inc/LBF_API. The cores of the functions are under …/libraries/BlueFrogV2-Lib/src/LBF_API.

Custom Type Definitions :

(from file custom_types.h)

typedef enum {
  FALSE = 0,
  TRUE = 1
}
boolean_t;

typedef enum {
  NOK = 0,
  OK = 1
}
ReturnStatus_t;

On-board LEDs and Slider Switch Control:

(from file LBF_LED_Switches_lowlevAPI.h)

void Stm32_Led_ON(void);
void Stm32_Led_OFF(void);
void Stm32_Led_TOGGLE(void);

boolean_t State_Switch1_IsOn(void);
boolean_t State_Switch2_IsOn(void);

Data Flash Control :

(from file LBF_FLASH_lowlevAPI.h)

void FLASH_EraseBulk(void);
void FLASH_WritePage(uint8_t* pBuffer, uint32_t WriteAddr, uint16_t NumByteToWrite);
void FLASH_WriteBuffer(uint8_t* pBuffer, uint32_t WriteAddr, uint32_t NumByteToWrite);
void FLASH_ReadBuffer(uint8_t* pBuffer, uint32_t ReadAddr, uint32_t NumByteToRead);
uint32_t FLASH_ReadID(void);

#define FLASH_PAGE_LENGTH 0x0100 // 256 bytes per page mode
#define FLASH_NUMBER_OF_PAGES 32768
#define FLASH_CAPACITY	(FLASH_PAGE_LENGTH * FLASH_NUMBER_OF_PAGES) // 32768 x 256B = 83888608 = 8MB = 64Mb

Direct STM32 GPIO Control :

(from file LBF_GPIO_lowlevAPI.h)

#define GPIO_HIGH(PORT,PIN) HAL_GPIO_WritePin(PORT, PIN, GPIO_PIN_SET)
#define GPIO_LOW(PORT,PIN) HAL_GPIO_WritePin(PORT, PIN, GPIO_PIN_RESET)
#define GPIO_TOGGLE(PORT,PIN) HAL_GPIO_TogglePin(PORT, PIN)

#define	IS_GPIO_SET(PORT, PIN)	(HAL_GPIO_ReadPin(PORT, PIN) == GPIO_PIN_SET)
#define	IS_GPIO_RESET(PORT, PIN)	(HAL_GPIO_ReadPin(PORT, PIN) == GPIO_PIN_RESET)

OLED Control :

(from file LFB_OLED_lowlevAPI.h)

#define OLED_CS_LOW() GPIO_LOW(OLED_CS_PORT, OLED_CS_PIN)
#define OLED_CS_HIGH() GPIO_HIGH(OLED_CS_PORT, OLED_CS_PIN)
#define OLED_RS_LOW() GPIO_LOW(OLED_RS_PORT, OLED_RS_PIN)
#define OLED_RS_HIGH() GPIO_HIGH(OLED_RS_PORT, OLED_RS_PIN)
#define OLED_RESET_LOW() GPIO_LOW(OLED_RESET_PORT, OLED_RESET_PIN)
#define OLED_RESET_HIGH() GPIO_HIGH(OLED_RESET_PORT, OLED_RESET_PIN)

/* Colors for OLED in rgb565 format */
#define BLACK	0x0000
#define WHITE	0xFFFF
#define RED	0xF800
#define GREEN	0x07E0
#define BLUE	0x001F
#define YELLOW	0xFFE0
#define CYAN	0x07FF
#define LIGHT_BLUE	0x1C9F
#define ORANGE	0xFD20

/* Screen dimensions - 160x128 for DD-160128FC-1A */
#define X_FULL_SCREEN 160
#define Y_FULL_SCREEN 128

/* OLED SPI */
uint8_t OLED_SPI_TransferByte (uint8_t octet);
void OLED_SendCmd (uint8_t Value);
void OLED_SendData (uint16_t Value);
void OLED_WriteReg (uint8_t RegName, uint8_t RegValue);
void OLED_DataStart (void);
void OLED_DataEnd (void);

/* OLED Gfx Generation */
void OLED_SetRegion(uint8_t x, uint8_t y, uint8_t width, uint8_t height);
void OLED_Fill(uint8_t x, uint8_t y, uint8_t width, uint8_t height, uint16_t color565);
void OLED_DisplayBuffer(uint8_t x, uint8_t y, uint8_t width, uint8_t height, uint16_t *buffer);
void OLED_Clear (void);

/* OLED High-voltage (14V) on/off control */
void OLED_Switch_ON (void);
void OLED_Switch_OFF (void);

/* « printf » type utilities – CAUTION : rely on emWin middleware, which mus therefore be enabled */
void OLED_Overwrite_CurrentLine(void);
void OLED_PrintString(char* string);
void OLED_PrintDec(int32_t SignedInteger);
void OLED_PrintHex(uint16_t Unsigned16);

/**** Note : for rich graphics and text generation, the emWin graphics library has a lot to offer ********/

Power Management

(from file LBF_PWR_lowlevAPI.h)

void Turn_VDDH_On(void);
void Turn_VDDH_Off(void);
boolean_t Check_VDDH_On(void);

UART (#1 and #3) Control

(from file LBF_UART_lowlevAPI.h)

void UART_SendData (UartID_t Uart_ID, uint8_t data);
uint8_t UART_ReceiveData (UartID_t Uart_ID);
void UART_SendString(UartID_t Uart_ID, char* pString); //!!Fix needed in there
void UART_SendString_SwFlowControl(UartID_t Uart_ID, char* pString); // !! Fix needed in there

typedef enum {
  UART1 = 1,
  UART3 = 3
}
UartID_t;

// For UART software flow control
#define XON 0x13
#define XOFF 0x11

I2C #2 Control

(from file LBF_I2C2_lowlevAPI.h)

void	I2C2_WriteSingleReg (uint8_t ChipID, uint16_t RegAdd, uint8_t RegVal);
void	I2C2_WriteMultipleReg (uint8_t ChipID, uint16_t RegAdd, uint8_t* pVal, uint16_t NumByteToWrite );

uint8_t	I2C2_ReadSingleReg (uint8_t ChipID, uint16_t RegAdd);
void	I2C2_ReadMultipleReg (uint8_t ChipID, uint16_t RegAdd, uint8_t* pVal, uint16_t NumByteToRead );

void	I2C2_RmodWSingleReg (uint8_t ChipID, uint16_t RegAdd, uint8_t RegMask, uint8_t RegUpdateVal);

Services

(from file Services.h)

void Delay_ms (volatile uint32_t nTime);

Pin aliases

(from file pin_aliases.h)

/* ==== Power Management ============================================== */

/* --- LTC3533 PMIC ---*/

//PC2 - HPWR, STM32 output
#define	HPWR_PIN	GPIO_PIN_2
#define HPWR_PORT	GPIOC

//PB6 - BUCK_ON, STM32 output
#define	BUCK3V_ON_PIN	GPIO_PIN_6
#define BUCK3V_ON_PORT	GPIOB

//PC13 - ONOFF_STAT (debounced On/Off push-button), STM32 input
#define	ONOFF_STAT_PIN	GPIO_PIN_13
#define ONOFF_STAT_PORT	GPIOC

/* --- TPS22929 Power Switch (DC-DC Boost Converter On/Off) ---*/

// PC0 - BOOSTCONV_EN, STM32 output
#define	VDDH_EN_PIN	GPIO_PIN_0
#define VDDH_EN_PORT	GPIOC

/* ==== LEDs ======================================================== */

// PC3 - STM32_LED, STM32 output
#define	STM32_LED_PIN	GPIO_PIN_3
#define STM32_LED_PORT	GPIOC

/* ==== Selection Switches =========================================== */

// PA15 - SWITCH1, STM32 input
#define	SWITCH1_PIN	GPIO_PIN_15
#define SWITCH1_PORT	GPIOA

// PC8 - SWITCH2, STM32 input
#define	SWITCH2_PIN	GPIO_PIN_8
#define SWITCH2_PORT	GPIOC

/* ==== I2C1 ======================================================== */

// PB8 - SCL, STM32 output, Open-Drain
// PB9 - SDA, STM32 output/input, Open-Drain
#define	I2C1_SCL_PIN	GPIO_PIN_8
#define	I2C1_SDA_PIN	GPIO_PIN_9
#define	I2C1_PORT	GPIOB

/* ==== I2C2 ======================================================== */

// PB10 - SCL, STM32 output, Open-Drain
// PB11 - SDA, STM32 output/input, Open-Drain
#define	I2C2_SCL_PIN	GPIO_PIN_10
#define	I2C2_SDA_PIN	GPIO_PIN_11
#define	I2C2_PORT	GPIOB

/* ==== SPI1 ========================================================= */

// PA5 - CK, STM32 output, Std CMOS
// PA6 - MISO, STM32 input
// PA7 - MOSI, STM32 output, Std CMOS
#define	SPI1_SCK_PIN	GPIO_PIN_5
#define	SPI1_MISO_PIN	GPIO_PIN_6
#define	SPI1_MOSI_PIN	GPIO_PIN_7
#define	SPI1_PORT	GPIOA

/* ==== SPI3 ========================================================= */

// PB3 - CK, STM32 output, Std CMOS
// PB4 - MISO, STM32 input
// PB5 - MOSI, STM32 output, Std CMOS
#define	SPI3_SCK_PIN	GPIO_PIN_3
#define	SPI3_MISO_PIN	GPIO_PIN_4
#define	SPI3_MOSI_PIN	GPIO_PIN_5
#define	SPI3_PORT	GPIOB

/* ==== UART1 ======================================================= */
// PA9 - TX, STM32 output, Std CMOS
// PA10 - RX, STM32 input

#define	UART1_TX_PIN	GPIO_PIN_9
#define	UART1_RX_PIN	GPIO_PIN_10
#define	UART1_PORT	GPIOA

/* ==== USART 2 ======================================================= */
// PA2 - TX, STM32 output, Std CMOS
// PA3 - RX, STM32 input
// PA4 - CK, STM32 output, Std CMOS

#define	USART2_TX_PIN	GPIO_PIN_2
#define	USART2_RX_PIN	GPIO_PIN_3
#define	USART2_CK_PIN	GPIO_PIN_4
#define	USART2_PORT	GPIOA

/* ==== UART 3 ======================================================= */
// PC10 - TX, STM32 output, Std CMOS
// PC11 - RX, STM32 input

#define	UART3_TX_PIN	GPIO_PIN_10
#define	UART3_RX_PIN	GPIO_PIN_11
#define	UART3_PORT	GPIOC

/* ==== DATA FLASH (excl SPI) ======================================== */

// PB7 = nCS
#define FLASH_CS_PIN	GPIO_PIN_7
#define FLASH_CS_PORT	GPIOB

/* ==== BTLE (excl UART) ======================================== */

// PC9 = BT_RST (active high)
#define BT_RST_PIN	GPIO_PIN_9
#define BT_RST_PORT	GPIOC

/* ==== LSM6DS3 ACCEL/GYRO ======================================== */

// PB15 = INT1_ACC_GYR, PC6 = INT2_ACC_GYR
#define INT1_ACC_GYR_PIN	GPIO_PIN_15
#define INT1_ACC_GYR_PORT	GPIOB
#define INT2_ACC_GYR_PIN	GPIO_PIN_6
#define INT2_ACC_GYR_PORT	GPIOC

/* ==== LIS3MDL MAGNETO ======================================== */

// PB13 = DRDY_MAG, PB14 = IRQ_MAG
#define DRDY_MAG_PIN	GPIO_PIN_13
#define IRQ_MAG_PIN	GPIO_PIN_14
#define MAG_PORT	GPIOB

/* ==== BATTERY ======================================== */

// PC1 = BATT_ADC_MEAS, PC7 = BATT_MEAS_EN
#define BATT_ADC_MEAS_PIN	GPIO_PIN_1
#define BATT_MEAS_EN_PIN	GPIO_PIN_7
#define BATT_PORT	GPIOC

/* ==== OLED (excl SPI) ======================================== */

// PC4 - OLED_RS, STM32 output
#define	OLED_RS_PIN	GPIO_PIN_4
#define OLED_RS_PORT	GPIOC

// PC5, OLED_NCS, STM32 output
#define	OLED_CS_PIN	GPIO_PIN_5
#define OLED_CS_PORT	GPIOC

// PB1 - OLED_RESET, STM32 output
#define	OLED_RESET_PIN	GPIO_PIN_1
#define OLED_RESET_PORT	GPIOB

Aliases for on-board chips (ID, registers, etc.)

(from file OnBoard_chip_aliasas.h)

// Magnetometer : ST LIS3MDL
#define LIS3MDL_CHIPID	0x1C
#define LIS3MDL_WHOAMI	0x0F
#define LIS3MDL_WHOAMI_CONTENTS	0x3D

// Accelerometer/Gyro : ST LSM6DS3
#define LSM6DS3_CHIPID	0x6A
#define LSM6DS3_WHOAMI	0x0F
#define LSM6DS3_WHOAMI_CONTENTS	0x69

// ALS/Proximity : ST VL6180X
#define VL6180X_CHIPID	0x29
#define VL6180X_WHOAMI	0x00
#define VL6180X_WHOAMI_CONTENTS	0xB4

// Pressure/Temp Sensor : ST LPS25H
#define LPS25H_CHIPID	0x5C
#define LPS25H_WHOAMI	0x0F
#define LPS25H_WHOAMI_CONTENTS	0xBD

Global Variables

(from file global_variables.h)

 /* ------- Handles on structures used by HAL API Functions ------------- */

extern UART_HandleTypeDef huart1;	// initialized in LBF_UART1_Init.c
extern USART_HandleTypeDef husart2;	// initialized in LBF_USART2_Init.c
extern UART_HandleTypeDef huart3;	// initialized in LBF_USART3_Init.c
extern I2C_HandleTypeDef hi2c1;	// initialized in LBF_I2C1_Init.c
extern I2C_HandleTypeDef hi2c2;	// initialized in LBF_I2C2_Init.c
extern SPI_HandleTypeDef hspi1;	// initialized in LBF_SPI1_Init.c
extern SPI_HandleTypeDef hspi3;	// initialized in LBF_SPI3_Init.c
extern TIM_HandleTypeDef htim4; // initialized in LBF_PWM4_Ch3-4_Init.c