Software Libraries
LBF
Set-up &
Initializations
Hardware
ARM CMSIS Lib
STM32L1xx HAL
Abstraction layer for all STM32L1 on-chip peripherals
La BlueFrog API
LBF
Utilities
User Application
BT 4.x
Profiles
USB Device
Stack
BT 4.x
Stack
FatFS
File System
EmWin
Graphics Lib
Ready-to-use Libraries
Provided. Open-source everywhere possible
Note : Various options available as real-time/embedded OS kernel if needed,
although not provided as part of La BlueFrog software package at this time.

---
Software Structure
/<xxxx>
-- /libraries
-- /BlueFrogV2-Lib
     # Board init and controls - La BlueFrog specific
     # Adaptation Layers for Middlewares (USBD, FatFS, emWin)
-- /CMSIS
-- /STM32L1xx_HAL_Driver
-- /STM32_USB-Device_Library
-- /FatFS_Lib
-- /STemWin_Lib
-- /projects
-- /Project-A
-- /inc
-- /src
-- Makefile
-- /obj
-- /Project-B
-- ..........
-- /Project-X
-- ..........
-- /STARTUP
-- startup_stm32l151xc.s
-- STM32151XC_FLASH.ld
-- /documentation
La BlueFrog libraries
ST- and 3rd-party supplied
libraries
Typically,
user would customize
these files

---
Software : BlueFrogV2-Lib Contents
/BlueFrogV2-Lib
   -- /src
-- /Board_Support
-- /LBF_API
-- /Debug_Utilities
-- /Sensor_APIs
-- /LBF_USB_MassStorage
-- /LBF_DataFlash_FatFS
-- /LBF_StemWin
   -- /inc
-- <same structure>
> IO configuration routines
> On-chip peripheral inits
> On-board chip inits
(fixed and selective – based on
user configuration files in /Project-xx)
Low-level API functions
For access to on-board hardware and busses (LED, Switches, Data Flash, I2C, ...)
Adaptation layer between ST-supplied middleware and La BlueFrog
(any file that is a « template » in ST deliverable or needed customization is here)

---
Software : User Project Contents
> Proposed template does full board initialization and leaves user concentrate on his/her application.
/projects
-- / <project name>
-- /main.c
-- /<other_user_files>.c
-- /stm32_it.c
-- /stm32_it.h
-- /User_Configuration.h
-- /IT_Priorities_UserDefinable.h
-- BriefDesc.txt
Interrupt request handlers
& associated callback functions.
Template proposed.
User defined configurations
(thru #define 's), esp. ::
- enable/assign extension header pins & related parameters (e.g. bitrates etc.)
- OLED and BTLE usage
User modifiable priorities of all LBF
potential interrupt sources.
All defined in this single central file.